## Slide 1: Flying Flashlight
May1738
Adviser: Dr. Gary Tuttle
Brady Koht - Team Leader
Joseph Wickner - Co-Team Leader & Co-Webmaster
Peter Bonnie - Group Communicator
Scott Melvin - Document Master
Sebastian Roe - Webmaster
Team Email – may1738@iastate.edu
http://may1738.sd.ece.iastate.edu

## Slide 2: Problem Statement
The Flying Flashlight team strives to design a portable, hands-free, drone based lighting system. Our target demographic will be varied as well as the implementation of our product. We view our product as a multi-purpose utility light.

## Slide 3: Requirements and Specifications
Functional
Size
Light Output
Lighting Modes
Tethered
Flight Stability
1 Hour Flight Time
7-10 Foot Flight Ceiling
Non-Functional
Safety Regulations
User Manual
Documentation

## Slide 4: Operating Environment
Outdoor Activities
Roadside Emergencies
Night Time/Low-Light Conditions

## Slide 5: System Block Diagram

## Slide 6: Wireless Communication
XBee series 1 Radio
  ISM 2.4 GHz Operating Frequency
  Data Rate = 250 kbps
  Indoor Range 100ft
  Outdoor Range 300ft

## Slide 7: System Analysis and Part Choices
MultiWii Pro vs. DJI Naza
Motors – Multistar Elite Racing 2204
ESC’s – Afro Race Spec
LED’s – Vollong 3W RGB
http://www.readytoflyquads.com/multiwii-pro-ez3-0-flight-controller-w-gps-option

## Slide 8: Propeller Choices
5x3
12.6V (3S): 50%=224g 3.7A, 100%= 371g 7.5A (Hover amps @ 125g thrust=1.7A (x 4=500g=6.8A) 8.4V (2S): 50%=120g 2.2A, 100%= 200g 4.3A (Hover amps @ 125g thrust=2.2A (x 4=500g=8.8A)
5x3x3 (3 blade)
12.6V (3S): 50%=232g 4.7A, 100%= 392g 9.9A (Hover amps @ 125g thrust=2.0A (x 4=500g=8A) 8.4V (2S): 50%=134g 2.7A 100%= 221g 6.7A (Hover amps @ 125g thrust=2.7A (x 4=500g=10.8A)
6x4
12.6V (3S): 50%=385g 7.5A, 100%= 591g 9.9A (Hover amps @ 125g thrust=1.4A (x 4=500g=5.6A) 8.4V (2S): 50%=230g 4.8A, 100%= 367g 9.7A (Hover amps @ 125g thrust=2.1A (x 4=500g=8.4A)

## Slide 9: Testing Plan

## Slide 10: Early Estimated Power Consumption
Assuming Quadcopter Weight at 360g
Flight Controller, MCU, etc. << 1W
LEDs 3W each. 4 LEDs = 12 W
Motor with 5x3 Prop
  Hovering Current = 1.7A @ 12.6V each
    Total Power = 85W providing 500g Lift
  Burst Current = 3.7A @ 12.6V each motor
    Total Power = 186W providing 896g Lift
Overestimated 97 W at Hover

## Slide 11: Power Consumption
Original frame: 383 g
Double Layer Frame: 383 g
Final Frame: 406 g
Hover Power = 78 W (vs 50.4 W estimate)
LED 100% Power = 23.28 W (vs 12 W estimate)
Total: 101.28 W (vs 97 W estimate)

## Slide 12: Basic LED PWM Control Schematic
PWM Control From Microcontroller
Vollong 3w RGB Common Cathode LEDS
P-Channel Power MOSFET Choices
  Fairchild FQP27P06
  Fairchild NDP6020P

## Slide 13: LIGHT DATA
 | Red (A) | Green (A) | Blue (A) | All 3 LEDs (A)
100% Brightness | 0.785 | 0.796 | 0.718 | 1.94
50% Brightness | 0.413 | 0.418 | 0.379 | 0.951
Max power consumption from the LED system alone is 23.28 Watts.
Graph data is taken from a distance of 3 feet to 2 inches away.

## Slide 14: PCB Design
Atmega328 Microcontroller
XBee Wireless Transceiver
Two voltage regulators: 5v and 3v3
LED driving MOSFETs

## Slide 15: PCB Design
Outer Power Plane: 12v
Inner Power Plane: 5v
Headers for Red, Green, Blue LEDs

## Slide 16: Winch Tether System

## Slide 17: Winch Tether System
Design work done in SolidWorks
  Lee Harker assisted with design
  Slip rings used to transfer power
Parts milled using CNC mill, performed by Lee Harker
  Aluminum used for end supports
  PVC, Acetal used for hubs/drum
  Gears supplied by ServoCity
  Slip rings supplied by DigiKey
  Bearings supplied by McMaster-Carr

## Slide 18
Frame Revisions

## Slide 19: Flight Testing
Accelerometer Calibration
PID Tuning

## Slide 20: Testing Results: LEDs & Communication
LED testing performed above expectations in terms of light output.
Power consumption was higher than anticipated.
Successful communication using two Arduino’s and Xbee’s to control the Quad

## Slide 21: Testing Results: Flight
Autonomous flight not achieved, not enough control
User controlled flight is better but the quad still requires more tuning and oscillation dampening

## Slide 22: Future Revisions
Different frame material
Different quad size
Flight controller
Control scheme