## Slide 1: Flying Flashlight
May1738
Adviser: Dr. Gary Tuttle
Brady Koht - Team Leader
Joseph Wickner - Co-Team Leader & Co-Webmaster
Peter Bonnie - Group Communicator
Scott Melvin - Document Master
Sebastian Roe - Webmaster
Team Email – may1738@iastate.edu
http://may1738.sd.ece.iastate.edu

## Slide 2: EE491

## Slide 3: Problem Statement
The Flying Flashlight team strive to design a portable, hands-free, drone based lighting system. Our target demographic will be varied as well as the implementation of our product. We view our product as a multi-purpose utility light.

## Slide 4: System Block Diagram

## Slide 5: Operating Environment
Outdoor Activities
Roadside Emergencies
Night Time/Low-Light Conditions

## Slide 6: Requirements and Specifications
Functional
Size
Light Output
Lighting Modes
Tethered
Flight Stability
1 Hour Flight Time
7-10 Foot Flight Ceiling
Non-Functional
FAA Regulations
Safety Regulations
User Manual
Documentation

## Slide 7: Deliverables
By end of Fall Semester
Prototype Drone
Propulsion System - 4 motors
Microcontroller communicating with flight controller
White flood light mode
Power provided by tethered external power supply
By end of Spring Semester
Final Prototype: Stable hovering LED platform
Different LED lighting modes
Control box with winch-like system and batteries
Operation Manual

## Slide 8: Work Plan

## Slide 9: System Analysis and Part Choices
MultiWii Pro vs. DJI Naza
Motors – Multistar Elite Racing 2204
ESC’s – Afro Race Spec
LED’s – Vollong 3W RGB
http://www.readytoflyquads.com/multiwii-pro-ez3-0-flight-controller-w-gps-option

## Slide 10: Testing Plan

## Slide 11: Prototyping

## Slide 12: Communications Demo

## Slide 13: Wireless Communication
XBee series 1 Radio
  ISM 2.4 GHz Operating Frequency
  Data Rate = 250 kbps
  Indoor Range 100ft
  Outdoor Range 300ft

## Slide 14: Test Fixture

## Slide 15: Propeller Choices
5x3
12.6V (3S): 50%=224g 3.7A, 100%= 371g 7.5A (Hover amps @ 125g thrust=1.7A (x 4=500g=6.8A) 8.4V (2S): 50%=120g 2.2A, 100%= 200g 4.3A (Hover amps @ 125g thrust=2.2A (x 4=500g=8.8A)
5x3x3 (3 blade)
12.6V (3S): 50%=232g 4.7A, 100%= 392g 9.9A (Hover amps @ 125g thrust=2.0A (x 4=500g=8A) 8.4V (2S): 50%=134g 2.7A 100%= 221g 6.7A (Hover amps @ 125g thrust=2.7A (x 4=500g=10.8A)
6x4
12.6V (3S): 50%=385g 7.5A, 100%= 591g 9.9A (Hover amps @ 125g thrust=1.4A (x 4=500g=5.6A) 8.4V (2S): 50%=230g 4.8A, 100%= 367g 9.7A (Hover amps @ 125g thrust=2.1A (x 4=500g=8.4A)
Current Quad Weight = 323g

## Slide 16: Estimated Power Consumption
Quadcopter weighs 323g => est. 360g Fully Loaded
Flight Controller, MCU, etc. << 1W
LEDs 3W each. 4 LEDs = 12 W
Motor with 5x3 Prop
  Hovering Current = 1.7A @ 12.6V each
    Total Power = 85W providing 500g Lift
  Burst Current = 3.7A @ 12.6V each motor
    Total Power = 186W providing 896g Lift
Overestimated 97W at Hover

## Slide 17: EE492

## Slide 18: Goals
LED Circuit Design, Prototype, & Test
Hovering & Flight Control Improvements
  Flight Test Fixture
Tether System
PCB’s Design and Printed.
Final Assembly

## Slide 19: Tether Control Box Sketch

## Slide 20: Basic LED PWM Control Schematic
PWM Control From Microcontroller
Vollong 3w RGB Common Cathode LEDS
P-Channel Power MOSFET Choices
  Fairchild FQP27P06
  Fairchild NDP6020P

## Slide 21: PCB Design
Atmega328 Microcontroller
XBee Wireless Transceiver
Two voltage regulators: 5v and 3v3
LED driving MOSFETs

## Slide 22: PCB Design II
Outer Power Plane: 12v
Inner Power Plane: 5v
Headers for Red, Green, Blue LEDs

## Slide 23: Winch Tether System

## Slide 24: Winch Tether System II
Design work done in SolidWorks
  Lee Harker assisted with design
  Slip rings used to transfer power
Parts milled using CNC mill, performed by Lee Harker
  Aluminum used for end supports
  PVC, Acrylic used for hubs/drum
  Gear supplied by ServoCity
  Slip rings supplied by DigiKey
  Bearings supplied by McMaster-Carr

## Slide 25: Flight Testing
Accelerometer Calibration
PID Tuning